## Slide 1
Institut for Parallel and Distributed Systems
Numerical Simulation
fluid solver for laminar flow with arbitrary geometries & heat flow
09.02.2021
[University of Stuttgart] [Stefania Scheurer, Marius Stach, Julian Franquinet]

## Slide 2: Task and Implementation
Numerical Simulation

## Slide 3: Heat Flow
Task
How to include temperature into code?
How to include temperature computation into solver?
What else to do?

## Slide 4: Heat Flow
Add computation of temperature T
Extend computation of velocities u and v by term contending T (heat transportation)
How to include temperature into code?
How to include temperature computation into solver?
What else to do?
Task

## Slide 5: Heat Flow
Task
Add field variable T for temperature
  As 2D array
Tij located at center of cell
  Size of T:
How to include temperature into code?
How to include temperature computation into solver?
What else to do?

## Slide 6: Heat Flow
Task
Computations of one timestep ():
How to include temperature into code?
How to include temperature computation into solver?
What else to do?

## Slide 7: Heat Flow
Task
Adapt criteria for computation of dt
Add parameters to input file
  (DonorCell), tInit (initial temperature of domain)
Extend outputwriter by adding new temperature array
How to include temperature into code?
How to include temperature computation into solver?
What else to do?

## Slide 8: Arbitrary Geometries and Obstacles
Underlying concept: flag matrix
How to include “real” boundary conditions?
How to include temperature?
What else to do?
How to apply boundary conditions at obstacles?

## Slide 9: Arbitrary Geometries and Obstacles
How to include “real” boundary conditions?
How to include temperature?
What else to do?
How to apply boundary conditions at obstacles?
Every cell assigned to type: FLUID, OBJECT, EMPTY
  Computation only for celltype FLUID
  Application of boundary conditions for celltype OBJECT:
    only NOSLIP boundary conditions for obstacles/objects
  Skip for celltype EMPTY
Underlying concept: flag matrix

## Slide 10: Arbitrary Geometries and Obstacles
1D arrays for each boundary (bottom, top, left, right)
  One array each for boundary condition type and value
1D array conceivable as mix of INFLOW, OUTFLOW, NOSLIP
How to include “real” boundary conditions?
How to include temperature?
What else to do?
How to apply boundary conditions at obstacles?
Underlying concept: flag matrix

## Slide 11: Arbitrary Geometries and Obstacles
Only NOSLIP, but different computation depending on FLUID surroundings of OBJECT cell
  OBJECT subdivided into types:
    -LEFT, -RIGHT, -TOP, -BOTTOM;
    -TOPLEFT, -TOPRIGHT, -BOTTOMLEFT, -BOTTOMRIGHT
How to include “real” boundary conditions?
How to include temperature?
What else to do?
How to apply boundary conditions at obstacles?
Underlying concept: flag matrix

## Slide 12: Arbitrary Geometries and Obstacles
How to include “real” boundary conditions?
What else to do?
How to apply boundary conditions at obstacles?
Underlying concept: flag matrix
Objects can be heated or isolated
  Two additional matrices for temperature boundary condition type (heated or isolated) and value (if heated)
Temperature at “real“ boundaries: extend 1D arrays by boundary type and value
How to include temperature?

## Slide 13: Arbitrary Geometries and Obstacles
Outputwriter uses staggered grid to write .vts files
  EMPTY cells are blanked
How to create the input .txt file for boundaries and obstacles?
How to include “real” boundary conditions?
How to include temperature?
What else to do?
How to apply boundary conditions at obstacles?
Underlying concept: flag matrix

## Slide 14: Input File for Boundaries and Obstacles
Numerical Simulation

## Slide 15: How to define boundary condtion types and values?
{
Type= Bottombound
Velocity= Dirichlet; 0; 0
Pressure= Neumann; 0
Temperature= Neumann; 0
Position = 0; 1
}
Input File: Example
location of boundary
boundary type& values (u;v)
boundary type and value (p)
boundary type and value (T)
physical starting and end value

## Slide 16: How to define obstacles?
{
Shape = Rectangle
Position = 0; 0; 1; 1
Temperature = Dirichlet; 1
}
Input File: Example
Shape of obstacle
Lower left and upper right corner
Temperature type and value
{
Shape = Ellipse
Position = 1; 1; 0.8; 0.5
Temperature = Neumann; 0
}
Shape of obstacle
Center and halfaxes
Temperature type and value
{
Shape = Triangle
Position = 0; 0; 0; 1; 0.5; 1
Temperature = Dirichlet; 5
Type = Fluid
}
Shape of obstacle
Corners of triangle
Temperature type and value
Fluid type to cut out shape of obstacle

## Slide 17: Examples
Numerical Simulation

## Slide 18: Standard Forms: Possible Obstacles
Settings
physSize: 10x2
nCells: 200x40
endTime: 15s

## Slide 19: Channel with a Step: Comparison for Obstacles
Settings
physSize: 10x2
nCells: 100x20
endTime: 500s
Our Solver
Other Solver

## Slide 20: Rayleigh-Benard: Comparison for Heat Flow
Settings
physSize: 8x1
nCells: 80x20
endTime: 100s
Our Solver
Other Solver

## Slide 21: Fountain: Combination of Obstacles and Heat Flow
Settings
physSize: 2x2
nCells: 40x40
endTime: 20s

## Slide 22: Beanmachine
Settings
physSize: 34x32
nCells: 170x160
endTime: 0.05s

## Slide 23: Labyrinth
Settings
physSize: 5x2
nCells: 40x20
endTime: 50s
Velocity
Temperature

## Slide 24: NumSim
Settings
physSize: 15x5
nCells: 180x60
endTime: 20s

## Slide 25: NumSim Flow
Settings
physSize: 15x5
nCells: 180x60
endTime: 20s
Velocity
Temperature

## Slide 26: City
Settings
physSize: 10x5, 15x5
nCells: 160x80, 240x80
endTime: 10s

## Slide 27
Stefania Scheurer, Marius Stach, Julian Franquinet
e-mail
enter address
phone +49 (0) 711 685-
www.
enter address
University of Stuttgart
Institut for Parallel and Distributed Systems